## Slide 1
NETWORK AUTOMATION BRIEFING
Zero-Touch Provisioning
From rack to ready
How an unconfigured switch finds its own IP, downloads its own instructions, and hands itself over to full automation — in two structured phases.
PHASE 1
Pre-Work & Planning
PHASE 2
ZTP & Automation

## Slide 2
Two phases, one seamless deployment
A structured hand-off from human planning to machine execution.
PHASE 1 — BEFORE ZTP
Pre-Work & Planning
Rack Builder
Reserves the exact physical port and rack location before install.
ServiceNow
Single source of truth — records every device serial and site.
Infoblox DDI
Auto-allocates management IPs and pre-stages DNS records.
Outcome: device staged and ready to be picked up by ZTP.
PHASE 2 — THE ZTP FLOW
Automated Bootstrap & Handover
Boot, DHCP & Bootstrap
Switch requests an IP, gets Option 67, downloads its Python script.
Ansible AAP Automation
Script hands off to AAP, which deploys the gold configuration.
Validation & Handover
Health is verified automatically and ServiceNow is updated.
Outcome: device active in production, fully validated.

## Slide 3
PHASE 1
Pre-Work: preparing before ZTP begins
Three systems establish identity, location, and network reservation before any device is powered on.
1
Rack Builder
SITE PLANNING
Ensures the switch is installed in the precise physical port and rack location.
2
ServiceNow
INVENTORY CMDB
Acts as the single source of truth for all device serial numbers and site metadata.
3
Infoblox DDI
IPAM & DNS
Automatically allocates management IPs and prepares DNS records for new devices.
PRE-WORK SEQUENCE
1
Rack Builder reserves the port & rack location
2
CAW file exported to the DC team for cabling
3
DC team adds the new device into ServiceNow
4
Device staged — ready to be picked up by ZTP

## Slide 4
PHASE 2
Connecting the switch to the automation engine
How unconfigured hardware uses DHCP and Python to bootstrap its own setup process.
1
Switch Initialization
Cisco or Arista switches without a startup configuration enter ZTP mode and initiate a DHCP request.
2
DHCP Server Response
The server responds with standard IP configuration and Option 67, specifying the boot-file name on the ZTP server.
3
Bootstrap Script Download
The switch downloads a Python bootstrap script that functions as the brain for the initial setup process.
4
Setup & Automation Handoff
The script identifies the switch serial number, verifies the OS version, upgrades if necessary, and hands control to Ansible AAP.

## Slide 5
PHASE 2
From automation to production handover
Ansible AAP takes control from the bootstrap script and drives the device to a validated, production-ready state.
Automation
Ansible AAP builds the full config from the switch serial number and deploys the gold configuration to the device.
Validation
The device reboots to trigger a post-build job; AAP performs automated certification and health verification.
Handover
Once validated, the device is marked active and ServiceNow is automatically updated with its final state.
Job triggers: code upgrade → config build (TOWER_CONFIG_TMPL_ID) → certification & validation (TOWER_VALIDATION_TMPL_ID) → post-build validation

## Slide 6
The 8-phase lifecycle of an automated deployment
A structured transition from physical installation to a fully validated production-ready state.
Phase 1 — Pre-Work
Phase 2 — ZTP & Automation
1
Planning
Reserve space and record serials in ServiceNow.
2
Network Prep
Infoblox creates DNS/DHCP records.
3
Device Boot
Switch requests IP via management network.
4
DHCP Response
Switch receives IP and bootstrap URL.
5
Bootstrap
Python verifies hardware and software.
6
Automation
Ansible AAP deploys gold configuration.
7
Validation
Automated verification of health.
8
Handover
Device active; ServiceNow updated.

## Slide 7
Seven core components power the ZTP ecosystem
A multi-vendor architecture bridging physical installation and automated management.
Component | Phase | Role | Why it is needed
Rack Builder | 1 | Site Planning | Ensures the switch is installed in the precise physical port and rack location.
ServiceNow | 1 | Inventory CMDB | Acts as the single source of truth for all device serial numbers and site metadata.
Infoblox DDI | 1 | IPAM & DNS | Automatically allocates management IPs and prepares DNS records for new devices.
DHCP Server | 2 | Option 67/150 | Directs the unconfigured switch to the ZTP server to retrieve its bootstrap instructions.
ZTP Server | 2 | File Hosting | Provides the initial Python bootstrap scripts and approved OS images to the switch.
Python Bootstrap | 2 | Logic Layer | Collects hardware-specific details and initiates the primary automation workflow.
Ansible AAP | 2 | Execution Engine | Generates the final configuration, applies it, and performs all health validations.

## Slide 8
Two phases. One self-provisioning switch.
Human planning establishes identity and reservation; automation takes it the rest of the way to production.
PHASE 1 · PRE-WORK
Rack Builder reserves the physical slot
ServiceNow records the device as the CMDB source of truth
Infoblox DDI pre-allocates IP and DNS records
Device is staged and ready for pickup
PHASE 2 · ZTP & AUTOMATION
Switch boots, requests DHCP, gets Option 67
Python bootstrap script downloads and runs
Ansible AAP deploys the gold configuration
Automated validation, then handover to production