## Slide 1
HLD / LLD · NETWORK AUTOMATION
Enterprise Zero-Touch Provisioning
From rack to production-ready
End-to-end provisioning for Cisco and Arista switches — integrating Rack Builder, ServiceNow, Infoblox DDI, DHCP, Python bootstrap, Git and Ansible Automation Platform (AAP) to eliminate manual configuration.
1
Phase 1: Pre-ZTP Preparation
2
Phase 2: ZTP Execution

## Slide 2
Purpose & solution overview
PURPOSE
Describes the end-to-end enterprise workflow for provisioning Cisco and Arista switches using Zero Touch Provisioning (ZTP), split into two major phases — Pre-ZTP Preparation and ZTP Execution — to eliminate manual switch configuration.
SOLUTION OVERVIEW
Provisioning begins long before a switch is powered on. Operational teams prepare rack assignments, reserve ports, register serials, and allocate management IPs. Once installed, the switch retrieves its bootstrap script, validates hardware/software, upgrades the OS if required, receives its production configuration, performs health validation, and updates enterprise inventory systems.
Rack Builder
ServiceNow
Infoblox DDI
DHCP
Python
Git
Ansible AAP

## Slide 3
Two phases, one seamless deployment
A structured hand-off from human planning to machine execution.
PHASE 1 — PRE-ZTP PREPARATION
Prepares all enterprise systems before the switch is connected.
Rack Builder
Reserve rack, RU position, management port; record vendor/model/serial.
ServiceNow CMDB
Create device record; store serial, site, rack, owner; track lifecycle status.
Infoblox DDI
Allocate management IP; create DNS records and DHCP reservation with Option 67/150.
Output: network infrastructure fully prepared — device ready for automated provisioning.
PHASE 2 — ZTP EXECUTION
Once the switch is powered on, the full ZTP workflow starts automatically.
Boot → DHCP → Bootstrap
Switch boots, discovers DHCP, and downloads bootstrap.py from the ZTP server.
Python → AAP Handoff
Script collects facts and calls Ansible AAP via REST API to deploy config from Git.
Validation → Handover
Health checks run, ServiceNow updates, monitoring begins, device goes production.
Output: switch fully configured and validated.

## Slide 4
PHASE 1
Pre-ZTP Preparation: three systems, three outputs
Objectives, activities and outputs for each pre-work system, per the LLD.
Rack Builder
Prepare the physical installation before the switch arrives.
ACTIVITIES
Reserve rack location (Rack/RU)
Reserve management switch port
Record serial number, model, asset tag
Verify cabling and power availability
OUTPUT
A deployment request is generated and forwarded for inventory registration.
ServiceNow CMDB
Maintain the source of truth for network assets.
ACTIVITIES
Create CMDB record
Store serial, vendor, model, site, rack, owner
Associate change request & deployment ticket
Track status: Planned → In Progress → Completed
OUTPUT
Validated inventory record ready for automation.
Infoblox DDI
Prepare networking services ahead of boot.
ACTIVITIES
Allocate management IP
Create forward/reverse DNS records
Configure DHCP reservation
Configure Option 67/150 with bootstrap URL
OUTPUT
Device can obtain all required network info during boot.

## Slide 5
PHASE 2
ZTP Execution — from power-on to bootstrap
Once powered on, the workflow starts automatically — steps 1 through 4.
1
Device Boot
The unconfigured Cisco/Arista switch powers on and detects the management interface, entering ZTP mode.
2
DHCP Discovery
The switch sends a DHCP Discover request. DHCP returns the management IP, subnet, gateway, DNS, and Option 67 pointing to bootstrap.py.
3
Bootstrap Download
Using the Option 67 URL, the switch securely downloads the Python bootstrap script from the ZTP server via HTTP/HTTPS.
4
Python Bootstrap
The script collects hardware inventory (serial, model, OS version, interfaces), validates software, installs root certificates if needed, and determines if an OS upgrade is required.

## Slide 6
PHASE 2
ZTP Execution — from automation to handover
Python hands off to Ansible AAP, which configures, validates, and closes the loop — steps 5 through 8.
5
Automation Handoff
Python invokes Ansible Automation Platform using REST APIs and passes all discovered facts.
6
Configuration Deployment
AAP generates a device-specific configuration from Jinja2 templates stored in Git, upgrades software if required, installs certificates, applies configuration and saves it.
7
Validation
Automated health checks verify interfaces, routing protocols, LLDP neighbors, port channels and overall operational status.
8
Handover
Deployment results are logged, ServiceNow is updated, monitoring begins and the switch is marked production ready.

## Slide 7
Detailed data flow
How data and control move across systems from reservation to production handover.
STEPS 1–5 — PREPARATION THROUGH FACT COLLECTION
1
Rack Builder → ServiceNow → Infoblox → DHCP
2
Switch Power On
3
DHCP Discover - options 67/43
4
Download bootstrap.py
5
Switch Info Collection
STEPS 6–10 — AUTOMATION THROUGH HANDOVER
6
REST API → Launch AAP Job
7
Downloads the configuration by Serial Number(From atwork)
8
Configuration Deployment
9
Validation
10
Ready to Use

## Slide 8
Component responsibilities
Nine systems span both phases of the ZTP workflow, each with a defined role and responsibility.
Component | Phase | Role | Responsibility
Rack Builder | 1 | Planning | Reserve rack position, ports and capture device information.
ServiceNow | 1 | CMDB | Maintain inventory and deployment lifecycle.
Infoblox DDI | 1 | IPAM / DNS / DHCP | Allocate IPs, DNS records and DHCP options.
DHCP Server | 2 | Bootstrap | Provide IP address and bootstrap URL.
ZTP Server | 2 | File Repository | Host Python bootstrap scripts and OS images.
Python Bootstrap | 2 | Discovery | Collect facts, validate device and call AAP.
Git | 2 | Source Control | Store templates, playbooks and configurations.
Ansible AAP | 2 | Automation | Upgrade software, deploy configuration and validate health.
Monitoring | 2 | Operations | Collect telemetry and ongoing health status.

## Slide 9
Benefits of the automated workflow
Six outcomes delivered end-to-end across both phases.
Completely automated Day-0 provisioning
Consistent configuration across all sites
Deployment time reduced from hours to minutes
Centralized inventory and audit trail
Automated software compliance and validation
Vendor-independent — supports Cisco and Arista

## Slide 10
Two phases. One self-provisioning switch.
Human planning establishes identity and reservation; automation takes it the rest of the way to production.
PHASE 1 · PRE-ZTP PREPARATION
Rack Builder reserves rack, RU and port
ServiceNow records the device as CMDB source of truth
Infoblox DDI allocates IP, DNS and DHCP Option 67/150
Device is staged and ready for automated pickup
PHASE 2 · ZTP EXECUTION
Switch boots, discovers DHCP, downloads bootstrap.py
Python collects facts and calls AAP via REST API
AAP deploys config from Git/Jinja2 templates
Validation runs, then handover to production + monitoring